## Slide 1
Inventor Events
Presenter
Developer Technical Services

## Slide 2: Agenda
Inventor Events
Events in VB.Net
Events in C#
Interaction Events

## Slide 3: Inventor Events
Events are notifications that Inventor sends when specific actions occur within Inventor.
Events allow your program to respond to incidents within Inventor.
By updating information in response to certain actions you can define your own associativity.
Provides for a mechanism for advanced interaction with the end-user.

## Slide 4: Inventor Events

## Slide 5: General Rules for Events
Private Sub oAppEvents_OnSaveDocument(ByVal DocumentObject As Document, _ ByVal BeforeOrAfter As EventTimingEnum, _ ByVal Context As NameValueMap, _ HandlingCode As HandlingCodeEnum)
End Sub
The first argument(s) provide information that is useful in the context of that event.
BeforOrAfter tells you if the event is firing before or after the action it is notifying you about. Some events fire only before, others fire only after, and most fire for both. Should always check for a specific time in case additional support is added in new releases.
Context provides other information related to this specific event. This is specific to each event and is not used by most events.
HandlingCode allows you to inform Inventor how the event is to be handled. Provides an opportunity for you to handle the event and perform the actions instead of Inventor, or to cancel and event. Not supported by most events.
Notes: Introduction to Event Context Information
The Autodesk Inventor API supports notification of many events. These events range across the entire API. Examples include notification of:
When a file is opened or closed.
When a browser node is activated or renamed.
When the mouse position is updated or keyboard input is received.
When a view or assembly is changed.
When objects are selected.
Currently there are more than 80 types of events fired, accessible from the API.
Events are the means through which your application is made aware of and reacts to actions outside its control. Events are also the basis for user interaction. If you want to trace mouse movement or know when a key has been pressed, your application must set up a handler for these specific events.
The Purpose of Event Context Information
The majority of events are straightforward - they simply provide notification that something has occurred. However, there are some situations when a little more information is required or some contextual information is helpful.
Consider when a file is dirtied, for example. The terms "dirtied" and "smudged" refer to the edit state of the document, somewhat analagous to paper drawings that have been manually revised. If changes have occured that would cause Autodesk Inventor to ask if you wish to save the file before exiting, that file is considered dirtied until saved. But some actions - a rebuild or the addition of client graphics, for example - do not affect the shape of the model, but can still be considered a change, or a "smudging" of the document. It can be useful to know such contextual information when an event occurs.

## Slide 6: Handling Events in VB.Net (VB Style)
Private WithEvents m_ApplicationEvents As ApplicationEvents
Public Sub Activate( ByVal addInSiteObject As Inventor.ApplicationAddInSite, _
ByVal firstTime As Boolean) _
Implements Inventor.ApplicationAddInServer.Activate
m_inventorApplication = addInSiteObject.Application
m_ApplicationEvents = m_inventorApplication.ApplicationEvents
End Sub
Private Sub m_ApplicationEvents_OnOpenDocument(ByVal DocumentObject As Inventor._Document, _
ByVal FullDocumentName As String, _
ByVal BeforeOrAfter As Inventor.EventTimingEnum, _
ByVal Context As Inventor.NameValueMap, _
ByRef HandlingCode As Inventor.HandlingCodeEnum) _
Handles m_ApplicationEvents.OnOpenDocument
System.Windows.Forms.MessageBox.Show("OnOpenDocument: " + DocumentObject.DisplayName)
End Sub

## Slide 7: Handling Events in VB.Net (VB.NET Style)
Private m_ApplicationEvents As Inventor.ApplicationEvents
Public Sub Activate(ByVal addInSiteObject As Inventor.ApplicationAddInSite, _
ByVal firstTime As Boolean) _
Implements Inventor.ApplicationAddInServer.Activate
m_inventorApplication = addInSiteObject.Application
m_ApplicationEvents = m_inventorApplication.ApplicationEvents
AddHandler m_ApplicationEvents.OnOpenDocument, _
AddressOf Me.m_ApplicationEvents_OnOpenDocument
End Sub
Private Sub m_ApplicationEvents_OnOpenDocument(ByVal DocumentObject As Inventor._Document, _
ByVal FullDocumentName As String, _
ByVal BeforeOrAfter As Inventor.EventTimingEnum, _
ByVal Context As Inventor.NameValueMap, _
ByRef HandlingCode As Inventor.HandlingCodeEnum)
System.Windows.Forms.MessageBox.Show("OnOpenDocument: " + DocumentObject.DisplayName)
End Sub

## Slide 8: Handling Events in C#
private Inventor.ApplicationEvents m_appEvents;
public void Activate(Inventor.ApplicationAddInSite addInSiteObject, bool firstTime)
{
// Initialize AddIn members.
m_inventorApplication = addInSiteObject.Application;
// Get a reference to the ApplicationEvents object.
m_appEvents = m_inventorApplication.ApplicationEvents;
// Create a delegate to handle the OnSaveDocument event.
m_appEvents.OnSaveDocument +=
new ApplicationEventsSink_OnSaveDocumentEventHandler(m_appEvents_OnSaveDocument);
}
// Handle the OnSaveDocument event.
void m_appEvents_OnSaveDocument(_Document DocumentObject,
EventTimingEnum BeforeOrAfter,
NameValueMap Context,
out HandlingCodeEnum HandlingCode)
{
// Code to respond to the event.
// It is required to fill the output parameters in C#
HandlingCode = HandlingCodeEnum.kEventNotHandled;
}

## Slide 9
Provides the standard Inventor command behavior
  Starting the InteractionEvents causes the current command to be canceled.
  You become the focus of end-user interaction.
  If the end-user starts another command it cancels your running InteractionEvents object.
Provides the ability to do advanced selection logic.
Support for interactive preview graphics.
Interaction Events

## Slide 10
InteractionEvents object is created using the CreateInteractionEvents method of the CommandManager.
The created InteractionEvents object is associated with the currently active document.
Creating the InteractionEvents object doesn’t have any effect on Inventor until you call it’s Start method.
Interaction Events

## Slide 11
Create InteractionEvents object.
Connect to the desired event sets.
Set properties of the various event sets to get the desired behavior.
Start the InteractionEvents object.
Listen for and react to the events.
Stop the InteractionEvents when finished and watch for the OnTerminate event.
Interaction Events - Workflow
Notes: You need to create an InteractionEvents object to “mark” the start of your command and to use selection.
Then you can listen to the events you need, like OnSelect, OnPreselect, OnMouseMove, OnTerminate so on…
You have to explicitly enable some of the events before you will be able to listen to them.
Then you can start the interaction, in which case e,g, the cursor will change to object selection and your event handlers will be called where you can react to them.
If the process was successful from your command point of view, e.g. the right objects have been selected, then you just stop the interaction. It’s always good to listen to the OnTerminate event, which is called both if the interaction was successful or if it was cancelled by the user (or starting another command).

## Slide 12
Implementing a child modeless Dialog
Public Class WindowWrapper
Implements System.Windows.Forms.IWin32Window
Private _hwnd As IntPtr
Public Sub New(ByVal handle As IntPtr)
_hwnd = handle
End Sub
Public ReadOnly Property Handle() As IntPtr _
Implements System.Windows.Forms.IWin32Window.Handle
Get
Return _hwnd
End Get
End Property
End Class
Private Sub DisplayAsChildDlg()
Dim myForm As New CustomForm
myForm.Show(New WindowWrapper(m_inventorApplication.MainFrameHWND))
End Sub
Notes: One issue with displaying a dialog is that by default it is independent of the Inventor main window. This can cause a few problems: the Inventor window can cover the dialog, when the end-user minimizes the Inventor window your dialog is still be displayed, and key presses that represent keyboard shortcuts are stolen by Inventor.
To get around these problems you can make the dialog a child of the Inventor window. The sample above does this by using the WindowWrapper utility class, shown below.

## Slide 13
CommandManager.Pick
Simplified entity selection
Pre-select and select events outside of InteractionEvents
Pick method
Public Sub GetSingleSelection()
' Get a feature selection from the user
Dim oObject As Object
oObject = m_inventorApplication.CommandManager.Pick(SelectionFilterEnum.kPartFeatureFilter, "Pick a feature")
MsgBox( "Picked: " & oObject.Name)
End Sub
Notes: Selection of entities is done through the Select Set or through InteractionEvents. The select set doesn’t provide any control and requires a object-action workflow. InteractionEvents provides full control and a lot of flexibility but is difficult to implement. The new Pick method provides the same workflow as InteractionEvents but is much easier to implement. There is less control and flexibility but for many cases it is enough. Instead of any events it’s just a function call that returns a single selected entity of the type specified.

## Slide 14: Lab: Events and User Interaction
Create an addin project that listens to a simple event, e.g. ApplicationEvents.
Create a class that listens to InteractionEvents and SelectEvents.
Use SelectEvents.OnSelect to display a MessageBox that indicates the type of the entity the user just selected.
Create a simple Form with a button to interact with your event class (Display the form as child modeless).

## Slide 15
Notes: Thank you!
Questions?